## Slide 1: Advanced Controls

## Slide 2: Computer Vision
Solving for Angles and Distances
  X-Axis Alignment
  Distance
Solutions
  Computer Vision (SolvePNP)
    Coprocessor
      Roborio
      Raspberry Pi (Preferred)
    https://www.chiefdelphi.com/uploads/default/original/3X/5/e/5e2fb8ce56e27d7f4f63a97731700e4684d550e4.pdf
  Limelight
    Raspberry Pi
    Software

## Slide 3: Limelight
Uses Network Tables
NetworkTable table = NetworkTable.getTable("limelight");
double tx = table.getNumber("tx", 0); // Angle Offset from Target
double ty = table.getNumber("ty", 0);
X Angle Offset Given
Solve for Distance
  Given
    Height from Ground
    Angle from Ground
  Find
    Distance using Trig
https://docs.limelightvision.io/en/latest/getting_started.html#basic-programming

## Slide 4: Control System
Analyzing and Predicting Behavior of Systems
  Heater
  Fan Speed
Application within FRC
  Predicting motor behavior
  Accounting for unexpected behavior
    Too much Voltage
Feedback Controller
  Applies Ideas Above
  Predicts and Accounts for unexpected behavior

## Slide 5: PID Controller
PID
  Proportional
    Error to 0
  Integral
    Area of curve between setpoint and output
  Derivative
    Slope to 0
PID Controller
  Kp * Error + Ki * Integral of Error + Kd * Derivative of Error

## Slide 6: Tuning a PID Controller

## Slide 7: Tuning a PID Controller
Set Kp, Ki, Kd to 0
Increase Kp until oscillate around Setpoint
Increase Kd without jittering
Increase Ki if settling above or below setpoint
  Feedforward is preferred
Feedforward
  kF * Setpoint

## Slide 8: PID Controller
WPILib
  PIDController pid = new PIDController(kP, kI, kD);
  motor.set(pid.calculate(encoder.getDistance(), setpoint));
  pid.setTolerance(5, 10);
  pid.atSetpoint();

## Slide 9: Feed Forward
SimpleMotorFeedforward feedforward = new SimpleMotorFeedforward(kS, kV, kA);
  https://docs.wpilib.org/en/stable/docs/software/advanced-control/controllers/feedforward.html
motor.setVoltage(pid.calculate(encoder.getDistance(), setpoint) + feedforward);

## Slide 10: Trajectory Generation
Interesting Improvement
Generate Trajectory
  Autonomous
  “Draw” routes”
Outline
  PID with Feedforward
  Drivetrain Subsystem
  Create Trajectory (TrajectoryGenerator)
  RamseteController
Docs
  https://docs.wpilib.org/en/stable/docs/software/advanced-control/trajectories/index.html
Tutorial
  https://docs.wpilib.org/en/stable/docs/software/examples-tutorials/trajectory-tutorial/index.html